Program:        pciexp.exe
Author:         NCR MPD
Purpose:        53C8xx Test Software

This software was written by NCR Microelectronics to develop and 
test new products.  NCR assumes no liability for its use.  This 
software is released to the public domain to illustrate certain 
programming techniques for the 53c800 family.

INTRODUCTION
	This program provides and example of how to "correctly" setup
and use and 53C8xx as a SCSI driver.  The program inits the chip and
an interrupt service routine to handle interrupt from of chip.  The
example script is a general purpose target driven script.  This
allows virtually any SCSI command to be executed with the same
script. 

PROGRAM LAYOUT
	The program is contained in four modules:
main.c          Contains all the code that inits the C8xx and the
		hardware.  All low-level communication with the chip
		is contained in this module.

commands.c	Contains the code to setup the tables and start the
		script to perform different SCSI commands.  

os.c		A simple menu driven program that calls the commands
		defined in commands.c.  A this level all SCSI details
		and hardware is hidden.

tools.c		Misc. software tools that are used by the rest of the
		program.

pci.c           Contains PCI specific routines

general.ss	This SCSI SCRIPTS used by this program.  This script
		is a totally target driven script that can handle
		many different SCSI commands.

	These modules are used to provide progressive levels of
abstraction from the hardware. Most of the functions in the first two
modules are contained in the device driver for a SCSI device.


DESIGN DETAILS
	The script that is executed by this program is totally target
driven.  The program just inits the locations of the command, data,
and message buffers and starts the script.  The script performs
whatever functions the target wishes.  In this way, any command can
be executed by just putting that command in the command buffer and
setting up the data buffer correctly for that command.
	All of the data is passed to the script using the
table-indirect addressing mode of the C8xx.  The DSA is initialized to
point at a table of counts and addresses to be used in the script
instructions.  The offsets into that table for the different buffers
are stored in the script.

SUPPORT FOR SCATTER/GATHER
	This program was not intended as an example on how to handle
Scatter/Gather type files requests. (Where many different pieces of
memory need to be written end-for-end to the disk)  However in
solving another problem, I provided one way this kind of transfer can
be done.
	This feature started out with the question "How do I handle
a drive that disconnects between each block on multiblock reads?"  In
other words if I request 10 blocks from the disk in one read command
and the drive sends the first 4 blocks, disconnects to seek to a new
track, reconnects, and then sends the rest of the data, what is going
to keep the script from getting a phase mismatch in the middle of
the one block move?  
	The first solution that comes to mind is to check the phase
after every block transferred. This works but how do you continue the
transfer where it was left off?  All we can tell in the script is that
the current phase is DATA_IN and we should jump back to the data move
routines.
	The solution used in this program is to have a separate table
entry for every block to be transferred.  After each block the script
modifies its offset in the table to point to the next table entry. 
This way each block that is read/written can go to a different
address and even be a different length.  
	Since we are now able to read data from many different places
to write to the disk or read from the disk and write to several
different places, this script can solve several scatter/gather
problems.